## Slide 1: כל מה שרצית לדעת על createCleanFile ולא העזת לשאול
* הכותרת מנוסחת בלשון זכר ונקבה כאחד אך מתייחסת בעיקר לנשים 

## Slide 2: Outline
Artifacts in MEG
createCleanFile (&more)
  LF
  Accelerations
  HB
Troubleshoot
Work Flow

## Slide 3: Introduction
MEG amplitudes are very low and even small artifacts can distort the recordings.
  LF
  Mechanical Vibrations
  Heart Beat
  Step Correction
These types of artifacts can be removed by recording external cues along with the MEG.
These external cues are then used to register the exact times or spectra of the artifacts and thus contain minimal risk of distorting the data.
Other methods:
  Filtering
  ICA

## Slide 4: How To … Default Values
Input_file = ‘c,rfhp0.1Hz’;
p = pdf4D(input_file);
chi = channel_index(p, {‘MEG’}];
MEG = read_data_block(p, [], chi);
meanMEG = mean(MEG);
plot(meanMEG’)
cleanCoefs = createCleanFile(p, input_file,'outFile', ‘cleanFile’, 'byLF', [] , 'Method', ’Global' , 'xClean', [4 5 6], 'chans2ignore',[] , 'byFFT', 0, 'HeartBeat', [], 'noQuestions', 0 , 'stepCorrect', 1, ‘maskTrigBits’, [], ‘ECG’, meanMEG, ‘cleanPartOnly’, [startT endT]);
save cleanCoefs cleanCoefs

## Slide 5: How To … Recommended Values
Input_file = ‘c,rfhp0.1Hz’;
p = pdf4D(input_file);
chi = channel_index(p, {‘MEG’}];
MEG = read_data_block(p, [], chi);
meanMEG = mean(MEG);
plot(meanMEG’)
cleanCoefs = createCleanFile(p, input_file, 'byLF', [] , 'Method', ’Adaptive' , 'xClean', [4 5 6], 'chans2ignore', [], 'byFFT', 0, 'HeartBeat', [], 'stepCorrect', 1, ‘Hbperiod’, []);
save cleanCoefs cleanCoefs

## Slide 6: Line Frequency

## Slide 7: Line Frequency

## Slide 8: ‘Global’ vs. ‘Adaptive’

## Slide 9: Mechanical Vibrations

## Slide 10: Mechanical Vibrations

## Slide 11: Mechanical Vibrations

## Slide 12: Mechanical Vibrations

## Slide 13: Heart Beats
Ventricles Depolarization
Ventricles Repolarization
Atrium Depolarization

## Slide 14: Heart Beats - Detection
numSD = 2.5 – Standard deviation for peak detection
Default Hbperiod = 1 sec (findHBperiod = true)
minPeakSize = 2.7 (MEG – mean(MEG)/sd)
biggest = 2 (*meanPeak)
smallest = 0.5
mni = 0.25
mxi = 2
Notes: Filter – 4 – 50 Hz ( 2 – 100)

## Slide 15: Heart Beats – Amplitude

## Slide 16: Heart Beats - Results

## Slide 17: Heart Beats - Results

## Slide 18: Heart Beats - Results

## Slide 19: All Cleanings – Frequency Domain

## Slide 20: All Cleanings – Time Domain

## Slide 21: Troubleshoot
warning('MATLAB:MEGanalysis:ImproperData','Heart beat signal not clear enough No HB cleaning done')
'MATLAB:MEGanalysis:unreasonableValue 'Too slow Heart beat periods in 305.6
'MATLAB:MEGanalysis:unreasonableValue
Too small Heart beat amplitude in 105.8
'MATLAB:MEGanalysis:unreasonableValue\n',...
  'Too large Heart beat amplitude in

## Slide 22: Troubleshoot - Jump

## Slide 23: Troubleshoot - stepCorrect

## Slide 24: Troubleshoot - cleanPartOnly
Look at the mean MEG
  fileName = 'c,rfhp0.1Hz';
  p=pdf4D(fileName);
  samplingRate = get(p,'dr');
  % read all the MEG channels
  chi = channel_index(p, 'meg');
  data = read_data_block(p, [], chi);
  tMEG = (0:size(data,2)-1)/samplingRate;
  figure
  plot(tMEG,mean(data))
Detect jump time or other artifacts interrupting the HB detection.

## Slide 25: Troubleshoot – Muscle & more

## Slide 26: Troubleshoot – Changing Parameters
Use ‘Hbperiod’
tryClean function:
  Change the Errors threshold (line 326).
findHB01 function:
  numSD = 2.5 – Standard deviation for peak detection
  Default Hbperiod = 1 sec (findHBperiod = true)
  minPeakSize = 2.7 (MEG – mean(MEG)/sd)
  biggest = 2 (*meanPeak)
  smallest = 0.5
  mni = 0.25
  mxi = 2

## Slide 27: Recommendations
Always look at the mean MEG before starting the cleaning process to detect jumps or other large visible artifacts
Always check your cleaning in the frequency domain (fftIdan) and in the time domain (compareHBclean).
Reversing the order of cleaning (HB first) might help HB peak detection
Save the variable cleanCoefs and use the function listErrorInHB

## Slide 28: Work Flow
Look at the mean MEG
No Jumps
Jumps
Stuck on other artifacts
Detect jump time and run with ‘cleanPartOnly’
Successful cleaning
Look at the PSD and ‘compareHBclean’
Consult Idan
Stuck on other artifacts
Cleaning passed OK
Stuck on HB cleaning
Try cleaning HB without xClean and then use xClean on the cleaned file
Look at the PSD and on compareHBclean
Run with ‘stepCorrect’

## Slide 29: Problems to be solved
ECG recording –amplitude issue
xClean - Balistocardiogram

## Slide 30: Thank you

## Slide 31: cleanCoefs
Holds information regarding the cleaning process.
cleanCoefs.HBparams.Errors – holds times of errors in the HB cleaning process.
tList = listErrorsInHB(cleanCoefs) – list the times at which there was a difficulty with finding Heart Beats.

## Slide 32: fft
Input_file = ‘c,rfhp0.1Hz’;
Clean_file = ‘xc,hb,lf_c,rfhp0.1Hz’;
file3 = [];
file4 = [];
file5 = [];
fftIdan(input_file, clean_file, file3, file4, file5);

## Slide 33: compareHBclean
compareHBclean('-file1', 'c,rfhp0.1Hz', '-file2', 'clean1_c,rfhp0.1Hz','-acc','both');
  More parameters are in the help of the function
Must have cleanCoefs in the directory

## Slide 34: Mean MEG
  fileName = 'c,rfhp0.1Hz';
  p=pdf4D(fileName);
  samplingRate = get(p,'dr');
  % read all the MEG channels
  chi = channel_index(p, 'meg');
  data = read_data_block(p, [], chi);
  tMEG = (0:size(data,2)-1)/samplingRate;
  figure
  plot(tMEG,mean(data))